## Slide 1: Accelerometer-based Respiratory Rate and Heart Rate Detection
Project by Giulia Demme, 60161A

## Slide 2: Overview
Experimental Setup
iPhone 15 accelerometer (~100 Hz, Phyphox app)
Subject in supine position, smartphone on chest POS1
Spontaneous breathing +
Controlled breathing at predefined frequencies
Respiration Rate Estimate
Heart Rate Estimate
Motivation & Objective
Respiratory and Heart Rate are key vital signs
Simple estimation using a smartphone’s triaxial accelerometer
Non-invasive monitoring
Subjects
Acquisitions
Breathing conditions
3 healthy subjects
5 recordings per subject
Total: 15 recordings
5 breathing conditions:
Spontaneous breathing
Slow breathing
Fast breathing
Breathing with apnea
Breathing with small movement
Dataset
../data/person2/person2_spontaneous.csv

## Slide 3: Preprocessing
Characteristics
Different offsets and amplitudes across axes
Z axis dominated by gravity
Start/end transients
Raw accelerometric signal
Trimming
Characteristics
Fixed 60s window
60s * 99.7Hz = 5982 samples
Central segment of the recording
Removes start/end artifacts
Normalization
Characteristics
Fixed 60s window
Central segment of the recording
Removes start/end artifacts
Format
Estimated fs
Triaxial accelerometric signal (3xN)
≈ 99.7 Hz

## Slide 4: Respiration Rate Detection
Low-pass filter  PCA  Time-domain analysis – Autocorrelation  RR
 Frequency-domain analysis – Power Spectral Density  Periodogram  RR
 Welch  RR
Pipeline
Low-pass filter
Low-pass filtering
(fc=0.7 Hz)
3x5982 signal
3x5982 signal
Respiration is a low-frequency process (typical range: 0.1 – 0.7 Hz, 6 – 42 breaths/min)
4th-order Butterworth low-pass
Zero-phase filtering (filtfilt)
PCA
PCA
3x5982 signal
1x5982 signal
Respiration spread across X, Y, Z axes
PCA combines axes into a single dominant component
PC1 captures maximum shared motion
Giulia Demme UNIVERSITA’ DEGLI STUDI DI MILANO

## Slide 5: Respiration Rate Detection
Low-pass filter  PCA  Time-domain analysis – Autocorrelation  RR
 Frequency-domain analysis – Power Spectral Density  Periodogram  RR
 Welch  RR
Pipeline
Time-domain analysis – Autocorrelation
Autocorrelation
Computed on PCA respiratory signal
Lag 0 discarded (trivial maximum)
Periodic peaks correspond to respiration cycle
2. Peak detection
First non-zero peak → fundamental period
Respiratory Rate
Detect the period T of the first peak locs(1)
 RR = 60 / T
../data/person2/person2_normal.csv
First peak in seconds: 7.8s
in samples: 779
RR: 7.68 breaths/min
my_autocorrelation
1x5982 signal
R 1x5981
lags 1x5981
my_findpeaks
peaks
locs

## Slide 6: Respiration Rate Detection
Low-pass filter  PCA  Time-domain analysis – Autocorrelation  RR
 Frequency-domain analysis – Power Spectral Density  Periodogram  RR
 Welch  RR
Pipeline
Frequency-domain analysis – Power Spectral Density
PSD estimation
Periodogram: high resolution, higher variance
Welch: averaged segments, smoother spectrum
Search band: 0.05 – 0.7 Hz (equivalent to 3-42 breaths/min)
3. Find dominant frequency inside the band fresp
Respiratory Rate
4. RR = 60 * fresp
../data/person2/person2_normal.csv
Frequency of maximum PSD: 0.12 Hz
 RR: 7.30 breaths/min
periodogram
1x5982 signal
pwelch
fdom_welch
fdom_per
Band 0.05-0.7 Hz

## Slide 7: Respiration Rate Detection Results
Low-pass filter  PCA  Time-domain analysis – Autocorrelation  RR
 Frequency-domain analysis – Power Spectral Density  Periodogram  RR
 Welch  RR
Pipeline
People | Slow | Fast | Spontaneous | Apnea | Movements
Person 1 | 6.09 / 5.84 / 6 | 14.88 / 14.60 / 15 | 3.70 / 3.65 | 7.30 / 5.84 | 31.65 / 5.11 / 4.38
Person 2 | 7.58 / 7.30 / 7.5 | 14.92 / 14.60 / 15 | 7.68 / 7.30 | Nan / 3.65 / 4.38 | 17.49 / 17.52 / 17.52
Person 3 | 4.85 / 4.38 / 5 | 30.36 / 29.93 / 30 | 13.00 / 13.14 | 14.8 / Nan / 13.14 | 16.34 / 9.49 / 16.06
Values shown as: Autocorrelation / PSD / Reference
CBP
Values shown as: Autocorrelation / PSD or
Autocorrelation / Periodogram / Welch

## Slide 8: Heart Rate Detection
Band-pass filter  Find peaks  Build template  Compute cross-correlation  HR
Pipeline
SCG signal (seismocardiography)
7/23
Mechanical vibrations of the chest wall
Measured by accelerometer
Each heart-beat  characteristic vibration pattern
  IVC: low amplitude, noise-sensitive
  AO: strong and repeatable peak
  AC: smaller and more variable
Beat-to-beat interval  heart rate

## Slide 9: Heart Rate Detection
Band-pass filter  Find peaks  Build template  Compute cross-correlation  HR
Pipeline
8/23
Band-pass filter & axis choice
AO
IVC
AC
Filter X, Y, Z and visually compare
Choose (MANUALLY) the axis with clearest SCG morphology (AO peaks)
Band-pass filter design
  Butterworth band-pass 5-25 Hz
  Removes respiration/motion (<5 Hz)
  Removes high-frequency noise (>25 Hz)
In this case, the most informative axis is Y

## Slide 10: Heart Rate Detection
Band-pass filter  Find peaks  Build template  Compute cross-correlation  HR
Pipeline
9/23
Find peaks
SCG (1x5982)
Physiological constraint
maxHR  minPeakDistance
120 bpm  50 samples
Find peaks
peaks
locs
Threshold T
Keep peaks > T
Goal: Detect candidate AO peaks on SCG

## Slide 11: Heart Rate Detection
Band-pass filter  Find peaks  Build template  Compute cross-correlation  HR
Pipeline
10/23
Build template & Compute cross-correlation
Goal: Peak detection produces false positives
Validate peaks using morphology consistency
peaks
Template construction
Cross-correlation
template
Keep peaks if |lag| < 30 ms
Extract a fixed window around each candidate peak
Average windows → SCG template
Compare each beat segment with the template
Correct AO peak → best match at lag ≈ 0

## Slide 12: Heart Rate Detection
Band-pass filter  Find peaks  Build template  Compute cross-correlation  HR
Pipeline
11/23
Compute Heart Rate
Goal: Estimate Heart Rate
AO-AO interval  cardiac period
Instantaneous HR  60 / AO-AO interval
Mean HR  mean of instantaneous HR

## Slide 13: Heart Rate Detection Results
People | Slow | Fast | Spontaneous | Apnea | Movements
Person 1 | Z axis 76.71 bpm | Z axis 74.04 bpm | Z axis 75.57 bpm | Z axis 78.77 bpm | Z axis 73.56 bpm
Person 2 | Z axis 68.71 bpm | Z axis 66.79 bpm | Z axis 69.36 bpm | Z axis 68.06 bpm | Z axis 70.86 bpm
Person 3 | Z axis 71.29 bpm | Z axis 80.72 bpm | Z axis 71.44 bpm | Z axis 71.17 bpm | Z axis 76.14 bpm
Values shown as: Most informative axis / HR
Band-pass filter  Find peaks  Build template  Compute cross-correlation  HR
Pipeline

## Slide 14: Apnea & Movements – Limitations
apnea
movement
No peaks
False RR ≈ 31 bpm
Apnea
No respiratory periodicity
RR undefined
HR estimation remains stable
Movements
Spurious periodicity
False RR estimates
HR robust to moderate motion
../data/person2/person2_apnea.csv
../data/person1/person1_movements.csv

## Slide 15
Thank you
https://github.com/GiuliaDemme/VariationalEncoderForHeartBeatClassification